## Slide 1: ISRO I-ROC-U Robotics Challenge

## Slide 2
INTRODUCTION
We are Team Drone-A-Charyas from REVA University, a group of aerospace engineering students specializing in autonomous robotics.
We have been selected for the ISRO I-ROC-U Robotics Challenge 2026, a national-level platform hosted by URSC.
Current aerial scouts struggle in GPS-denied planetary environments; our mission is to build a "space robot" that navigates these terrains without human or satellite assistance.

## Slide 3
ABSTRACT
ASCEND (Autonomous Surveyor for Exploration, Navigation, and Dynamics) is a high-agility micro-quadrotor designed for fully autonomous mapping and feature detection.
The system runs a ROS2 perception stack on a Raspberry Pi 4, interfaced with a Pixhawk flight controller for precise, offboard mission logic.
We’ve integrated a unique servo-mounted TF-Luna LiDAR to generate 2D ground profiles, improving terrain feature matching by 25% in simulations.
A custom pogo-pin docking station allows the drone to land, transfer data, and fast-charge autonomously, supporting 4–5 sorties within the mission time limit.
The design includes a dual-IMU fusion failover system, reducing navigation failure rates to less than 2% during high-vibration flight

## Slide 4
PROJECT OBJECTIVES
Autonomous Navigation: Develop a micro-quadrotor capable of systematic search and feature detection in GPS-denied environments.
Persistent Operation: Enable multiple mission sorties through an autonomous docking and fast-charging system.
Reliable Perception: Utilize a unique servo-mounted LiDAR system to improve terrain mapping accuracy by 25% over static configurations.
Data Integrity: Facilitate secure, high-bandwidth data transfer via a wired UART interface upon successful docking.

## Slide 5
OUR SOLUTION
Modular Architecture: We are integrating a Raspberry Pi 4 companion computer with a Pixhawk flight controller to separate high-level autonomy from low-level flight stability.
Sensor Fusion: Our system fuses data from a 12MP wide-angle camera and a TF-Luna LiDAR to perform Simultaneous Localization and Mapping (SLAM).
Custom Docking Interface: We have designed a funnel-guided docking station using 6-pin spring-loaded pogo pins for automated power and data connectivity.
Validated Logic: All mission routines, including "Return-to-Base" and low-battery failsafe's, are first verified through Software-in-the-Loop (SITL) simulations before physical deployment.
Power Management: A 4S Battery Management System (BMS) is utilized to ensure safe CC/CV charging and to isolate sensitive electronics during the recharge cycle.

## Slide 6
SYSTEM SPECIFICATION
Sl. No. | Description | Specification
1 | Overall mass | Approx. 1.8-1.9kg all‑up (S500 frame ≈405 g + 4×A2212 motors + 4S 4500 mAh battery + electronics).
2 | Overall dimensions | Frame wheelbase: 500 mm motor‑to‑motor diagonal; landing gear height ≈200 mm;
3 | Power requirements | Flight power: 4S 14.8 V Li‑Po, 4500 mAh; peak system current typically <60–70 A; dock charging: 24 V input → 16.8 V CC/CV via buck + BMS.
4 | Flight time per charge | 8–10 minutes per sortie under typical mission profile (hover + slow translation) for 4S 4500 mAh on S500‑class quad.
5 | Number of propellers and their size | 4 propellers (quad configuration), 10″ fixed‑pitch (10×4.5)
6 | Features | - Autonomous takeoff, waypoint navigation, and landing via Pixhawk‑class FC and companion computer. - Automatic return‑to‑dock, funnel‑guided alignment, and pogo‑pin based charging with 4S BMS. - Onboard camera + range sensor for perception and obstacle/terrain sensing. ​ - Wired UART data link at dock plus wireless telemetry (RF) for monitoring, data sending and control.
7 | Others | - Safety: BMS‑managed 4S Li‑Po charging (CC/CV, cell balancing, over‑voltage/over‑current protection).

## Slide 7
COST OF THE COMPONENT
Mechanical Components
Electrical & Control Hardware
Sensors
Base Station & Docking Interface
No. | Hardware | Cost(in INR)
1 | Frame | 3000
2 | Motors | 2000
3 | Propellers | 120
4 | Sensor mounts | 1200
No. | Hardware | Cost(in INR)
5 | Battery | 5200
6 | ESCs | 6000
7 | Flight Controller | 20000
8 | Raspberry pi (2pc) | 20000
9 | Wiring & connectors | 500
No. | Hardware | Cost
10 | Barometer | 200
11 | Camera | 7000
12 | Range sensor | 5000
No. | Hardware | Cost
13 | Pogo-pin module | 600
14 | Base PCB | 2000
15 | UAV dock PCB | 2000
16 | 4S Li-Po BMS Board | 300
Total Cost = ₹75120

## Slide 8: THANK YOU